## Slide 1: PWM DRAWER
Prepared by: Ahmed Mohamed

## Slide 2: OUTLINES
Layered architecture
Flow chart
Measuring signal
LCD

## Slide 3: Layered Architecture
Application layer: Pwm Drawer
Hardware layer: LCD
Micro-Controller layer: Pwm – ICU - DIO

## Slide 4: Flow chart
Initialization
Init PWM
Init ICU
Init LCXS
Measuring signal
Get duty cycle
Get time
Get frequency
LCD
Display duty cycle
Display frequency
Display Time

## Slide 5: Measuring signal
Clear ICF , Trigger : raising edge
Waiting input capture ( POOLING )
Clear ICF , Trigger : falling edge
Waiting input capture ( POOLING )
Clear ICF , Trigger : raising edge
Waiting input capture ( POOLING )
Duty cycle = (high / period ) * 100
Frequency = F_CPU / period
Time = 1000000 / Frequency

## Slide 6: LCD
void LCD_Write_Str_4bit(char*str);
void LCD_Write_Num_4bit(int num);